## Slide 1
8-BIT Microprocessor
Digital Design using FPGA
Supervised by: Eng. Mohamed Salah Abo Shosha

## Slide 2
Mohamed Taha
Samuel
Haya Mahmoud
Khaled Eldaoudy
Project Team
Amr Saad

## Slide 3
What is an Accumulator CPU?
It is a minimalist microprocessor architecture where all arithmetic and logical operations center around a single main register called the Accumulator.
Unlike complex Register-to-Register models, this design simplifies the instruction set, reduces control logic overhead, and serves as an excellent foundation for understanding core digital CPU mechanics.
Introduction & Concept

## Slide 4
8-Bit Data Width
All internal data buses, the Accumulator, and memory words are strictly 8 bits wide, providing a clear and manageable scale for Verilog synthesis and waveform debugging.
Clean 8-Bit Instruction Format
Every instruction is exactly 8 bits. The first 4 bits represent the Opcode (the command to execute), and the remaining 4 bits represent the Address/Operand. Highly deterministic execution!
The Architecture & Idea

## Slide 5
The Heart of the CPU
The Accumulator is the primary 8-bit register that stores intermediate mathematical results. Every ALU operation inherently reads from and writes back to this specific register.
Benefit: Drastically simplifies the datapath routing and eliminates the need for complex multiplexers found in multi-register files, completely avoiding Read-After-Write (RAW) data hazards.
Component 1: The Accumulator (ACC)

## Slide 6
Mathematical Execution Engine
The ALU executes the core mathematical and logical instructions decoded from the software, such as ADD, SUB, AND, and NOT.
Benefit: It offloads raw computation from the central control logic. Designed to strictly interact with the Accumulator, ensuring clock-cycle precise data stability.
Component 2: Arithmetic Logic Unit (ALU)

## Slide 7
Sequential Tracking
An internal counter that holds the memory address of the next instruction to be fetched from RAM/ROM.
Branching & Jumps
Can be overwritten by the Control Unit to execute jump instructions, altering the flow of the program.
Benefit
Ensures orderly, clock-synchronized program execution without missing or skipping vital software steps.
Component 3: Program Counter (PC)

## Slide 8
Component 4: Control Unit
The Brain of the CPU
Implemented as a sophisticated combinational decoder (or FSM), it reads the 4-bit Opcode and generates absolute control signals for the entire datapath.
Benefit: It seamlessly orchestrates when the ALU calculates, when the PC increments, and when memory is read, bringing the raw logic components to life.

## Slide 9
Instruction & Data Storage
Accessed via a clean 4-bit address bus. Memory holds the compiled machine code instructions as well as raw data variables required by the CPU operations.
Programmability
Benefit: By separating memory from the execution logic, the CPU becomes a truly programmable device capable of running different software sequences without altering hardware.
Component 5: Memory (RAM/ROM)

## Slide 10
Step 1
Directory Setup (src/ & sim/)
Step 2
Code Core Modules (ALU, ACC, PC)
Step 3
Top-Level Integration & Control Unit
Step 4
QuestaSim Waveform Verification
Steps of Execution

## Slide 11
Thank You!
Ready for any question
Supervised by: Eng. Mohamed Salah Abo Shosha